## Slide 1: Sunday, 19 May 2024 Electrical circuits
By the end of the lesson you will be able to
Draw the circuits you build using correct symbols
Describe what current is

## Slide 2: Which ones won’t work?

## Slide 3: Will the bulb light?

## Slide 4: Will the bulb light?

## Slide 5: Will the bulb light?

## Slide 6: ammeter

## Slide 7: bulb or lamp

## Slide 8: switch

## Slide 9: cell

## Slide 10: voltmeter

## Slide 11: Circuit symbols

## Slide 12
A simple circuit showing electron flow.

## Slide 13: What is the energy change which takes place in a battery?
Chemical to Electrical

## Slide 14: Electrical Charge
Electric charge is given the symbol
Q
Electrons are the charge carriers
that flow in an electrical circuit –
from the negative to positive terminals.
2.21 mins https://www.youtube.com/watch?v=oB1v-wh7EGU

## Slide 15: Electrical Charge EXTENSION
Electrons are so very, very tiny that we measure large groups of them called coulombs. There are 6.25 x 1018 electrons in one coulomb.
The charge on one electron is 1.6 x 10-19 coulombs (C)

## Slide 16: Electrical Charge
The charge on a electron is
1.6 x 10-19C

## Slide 17: Charge, Current & Time
Electric current is given the symbol
I
Current is the amount of charge flowing per second and is given the unit
Amps (A)

## Slide 18: Experiment to measure current in series
Set up a series circuit with two 12v bulbs and a powerpack with a switch. Measure the current flowing at points 1, 2 and 3
ammeter
12v

## Slide 20: Working out power

## Slide 21: Calculate the power
1. A series circuit had a current of 2.0 amps and the voltage of the bulb is 3.0 volts. Calculate the power.
2. A series circuit had a current of 4.5 amps and the voltage of the buzzer is 2.0 volts. Calculate the power.

## Slide 22: Yesterday’s results

## Slide 23: Experiment to measure voltage in series
Add the voltmeter to the following components and record the voltage:
Bulb 1
Bulb 2
ammeter
12v

## Slide 24: Can you find the mistakes in this paragraph about current?
Current is the amount of electricity flowing around a circuit. We measure current using an Amp. Current is measured in Volts. The current is the same anywhere in a circuit, so it does not matter where an ammeter goes in a circuit. Current is used up as it goes around the circuit.

## Slide 25: Summary
 | CURRENT | VOLTAGE
Measured in |  | 
Measure with |  | 
Amps, A
Voltmeter
Ammeter
Volts, V

## Slide 26: Measuring Voltage in series circuits
Measure the voltage across the supply Vs
Measure the voltage across the first light bulb V1
Measure the voltage across the second light bulb V2
Write an equation connecting Vs, V1,and V2

## Slide 27: Summary
 | Series | Parallel
Current | SAME | SPLIT
Voltage | SPLIT | SAME

## Slide 28
The coulombs start with (for example) 12J of energy each.
They have “electrical potential energy”.
When the coulombs have travelled back to the battery they have transferred all their energy to other forms.
As the coulombs travel round the circuit this energy is changed to other forms.

## Slide 29: Where does most of the energy tranformation take place?
In the conducting wires the coulombs lose very little energy as the wires are made of a conductor (copper).
The light-bulb filament is made of resistance wire and this causes the coulombs to lose most of their energy in the bulb.
When the coulombs get back to the battery they have transferred all of their electrical potential energy and have no energy left.

## Slide 30: What has “potential difference” got to do with voltage?
It is the same thing!
The potential difference (p.d.), or voltage (unit volts),of a battery or cell is a measure of the electrical energy given to one coulomb of charge passing through the battery.
Voltage = energy per coulomb
V = E/Q

## Slide 31: Potential Difference or Voltage (V)
A 9 V battery will give how much energy
to each coulomb of charge passing
through the battery?
9 J
Now try some questions on the worksheets

## Slide 32: How can we measure voltage?
Voltage (or p.d.) can be measured using a
voltmeter.
An ammeter is connected
in the circuit in series.
but a voltmeter must be connected across (hug)
the component (in parallel).
V

## Slide 33: You can’t measure voltage…
in a circuit
through a circuit
through a component
flowing

## Slide 34: Tuesday
Insulation experiment
POWER

## Slide 35: Let’s watch this video before we do the INSULATION experiment.
https://www.youtube.com/watch?v=cYifAaTFe8A
3.21 mins

## Slide 36: Wednesday
Recap voltage current and power.
Calculations
Intro series and parallel

## Slide 37: Friday
Recap series and parallel
Investigation and design challenge

## Slide 38
7J Connecting circuits – Switch on

## Slide 39: Your Task
Design a circuit that can test for faulty components.
Design circuit
Draw circuit using symbols in our book
Explain how to use it

## Slide 40: Conventional current
Very unfortunately when electricity was discovered the physicists decided that the charge flowing was positive!!!!!
We still use this conventional current but it really doesn’t make any difference which way the current flows !

## Slide 41: Electrical Charge
Electric charge is given the symbol
Q
Electrons are the charge carriers
that flow in an electrical circuit –
from the negative to positive terminals.
2.21 mins https://www.youtube.com/watch?v=oB1v-wh7EGU

## Slide 42: Electrical Charge EXTENSION
Electrons are so very, very tiny that we measure large groups of them called coulombs. There are 6.25 x 1018 electrons in one coulomb.
The charge on one electron is 1.6 x 10-19 coulombs (C)

## Slide 43: Electrical Charge
The charge on a electron is
1.6 x 10-19C

## Slide 44: Kichoff’s first law
The current is the same at all points in a series circuit
Charge (electrons) don’t get used up.
Charge is conserved.

## Slide 45: Charge, Current & Time
If current is charge flowing per second then
time in seconds (s)
Current in Amps (A)
Charge transferred in coulombs (C)
so a current of 1 A is 1 C of charge transferred in 1 s.
Try the worksheet

## Slide 46: Now try some questions
GCSE bitesize questions

## Slide 47: Senior physics video potential difference

## Slide 48: When a battery is in a circuit…
The electrical energy is carried by the
electrons that move round the circuit.
It is converted into others forms of
energy.

## Slide 49: Energy is conserved
The voltage of the supply is the energy given to each Coulomb.
The voltages across each bulb is the energy lost by each coulomb as it travels through.
If we can ignore the conducting wires then by conservation of energy
Vs =V1+V2

## Slide 50: Measuring Voltage in a parallel circuit
Put the power pack on 12v
Connect two bulbs in parallel.
Measure the voltage of the supply Vs
Measure the voltages across each bulb V1 and V2.
What conclusion can you draw?
Can you explain these results?

## Slide 51: Voltage law in parallel
Vs =V1=V2
The coulombs can only travel through one branch of the parallel circuit so they must lose most of their energy there.

## Slide 52: What happens if we add more bulbs in parallel? Will they all have the same voltage across them?
Try it and see!

## Slide 53: Revision GCSE bitesize
Or go to the website furry elephant
User name jackie
Password medlock
Go to the lesson on current and voltage
There are some nice animations and also you can choose games and quizzes.

## Slide 54: Disadvantages of Series Circuits
When one component breaks the whole circuit stops working as no current flows.
The voltage is divided between the bulbs. so the more bulbs added the dimmer each one is.
The components can’t be switched on and off separately

## Slide 55: Advantages of a Parallel Circuit
When one bulb breaks the rest of the circuit
continues to work.
The voltage in each branch is the same as
the supply voltage. Therefore, bulbs in parallel
will each be as bright as a single bulb.
Each component can be switched on and off separately.

## Slide 56
Electrical Resistance
By the end of this lesson you should be able to:
Understand that the current in a series circuit depends on the applied voltage and the number and nature of other components.
Describe the qualitative effect of changing resistance on the current in a circuit
Recall and use the relationship between voltage, current and resistance

## Slide 57: Resistors
The ciruit symbol for a resistor is
Notes: 57
57

## Slide 58: Electron flow and Resistance
As the electrons move along the wire they collide with the metal atoms. These collisions make the atoms vibrate more which makes the metal hotter.
Resistance is a measure of how much a material tries to stop electricity passing through it.
4 mins https://www.youtube.com/watch?v=ue6w5aXhxjU

## Slide 59: Resistors Use these words to fill in the gaps below: insulators, copper, current, heat, resistors, conductors, alloys
Conductors such as cables have very little resistance and so very little electrical energy is changed to .
have very, very large resistances and so no________ can flow.
are inbetween.
They allow current to flow but not as well as____________
The bigger the resistance the smaller the __________
(for the same voltage).
Resistance wires are made of a mixture of metals e.g nichrome or constantin
copper
heat
Insulators
current
Resistors
conductors
current
alloys
Notes: 59
59

## Slide 60: Definition of Resistance
The resistance of a resistor is defined as the voltage across the resistor divided by the current flowing through it.
Resistance = voltage
current
Volts v
Amps A
OhmsW
Ohm’s law
Notes: 60
60

## Slide 61
Measure some resistances:
Put the power pack on 10v.
Measure the current and the voltage across a metal resistor.
Voltage = __________
Current = __________
Resistance R =V/I = ___
Find the resistance of a light bulb in the same way.
Find out what happens to the total current flowing when you put both the light bulb and the resistor in series.

## Slide 62
decreases
What can you say about current and
resistance for a fixed voltage?
As resistance increases, the current…..
decreases
As resistance decreases, the current …..
increases
Notes: 62
62

## Slide 63: Using Ohm’s law:
For a voltage of 12V, calculate the
current for a resistance of
4 Ω
24 Ω
1 k Ω
Notes: 63
63

## Slide 64: Resistance for a bulb
If you have a filament bulb and it has a current of 20A running through it, with a potential difference of 100V across it, what is the resistance of the bulb?
V = IR
R = V/I
R = 100V/20A
R = 5 

## Slide 65: Formula triangles
V
I
R


x
Formula triangles help you to rearrange formula, the triangle for the Ohm’s Law is shown below:
Whatever quantity you are trying to find cover it up and it will leave you with the calculation required.
So if you were trying to find current, I…..
…you would cover I up…
…and you are left with the sum…
I = V
R

## Slide 66: Varying Resistance
A variable resistor can be used to vary the current in a circuit
Notes: 66
66

## Slide 67: Current for a diode
A diode has a current of 5A running through it, and a resistance of 5. What is the potential difference across the diode?
V = IR
V = 5A x 5
V = 25V

## Slide 68
By the end of the lesson you should be able to:
Describe how current varies with voltage in wires, resistors, metal filament lamps and diodes, and how this can be investigated experimentally.
Lesson 2 and 3
Investigating how current varies with voltage for 3 different circuit components

## Slide 69: Experiment to investigate I/V curves for a resistor, a filament and a diode.
Voltage V | Current I
Fixed resistor
rheostat
In this circuit the rheostat is being used as a voltage divider

## Slide 70: Variable Resistors
A
lamp
What do you expect
to happen to the current and the brightness of the bulb if you increase the value of the resistor in the circuit shown?
cell
Variable resistor
Notes: 70
70

## Slide 71: Relationship between current and voltage in a fixed resistor
current / Amps
voltage (volts)
A straight line through
the origin tells us that current is directly proportional to voltage
The ratio V/I is the reciprocal of the gradient. It is equal to the resistance of the resistor.
A metal resistor has a constant resistance.But only if the temperature stays constant
The gradient of the line gives us the ratio of I/V.
Notes: 71
71

## Slide 72: I/V curve for a light bulb
The gradient is decreasing and so the resistance of the filament must be increasing.
The current is increasing as voltage increases but not as much as for a constant resistance.

## Slide 73: Filament Lamp
Electric current
passes through the
resistance wire which
is made of tungsten.
Electrical energy is
changed into heat
energy and the
wire glows white hot.
Filament lamps
produce both heat and
Light.
Notes: 73
73

## Slide 74
In the fixed resistor, current and voltage are directly proportional. But for a light bulb as the current increases, the electron/ion collisions causes the ions to vibrate more (the filament heats up). This increases electron/ion collisions even more and so the resistance of the filament increases every time the current increases.
I/V curve for a light bulb
Notes: 74
74

## Slide 75: I/V curve for a diode
Diodes only let current flow through them in one direction. They can be used to show that current is flowing in a circuit and in which direction.
Diodes are also used to change alternating current to direct current
The arrow shows the direction of conventional current when the diode conducts.

## Slide 76
Resistors in series and parallel
How does the total resistance of a circuit change if we connect:
More than one resistor in series?
More than one resistor in parallel?

## Slide 77
Lesson 4
By the end of the lesson you should be able to:
Describe the qualitative variation of resistance of LDRs with illumination and of thermistors with temperature.
Experiment sheet to investigate the properties of LDRs and thermistors.
Special Resistors

## Slide 78: Light Dependent Resistors
The resistance of an LDR decreases as the light intensity increases

## Slide 79: Thermistors
The resistance of a thermistor dcreases as the temperature increases

## Slide 80
Circuits Quiz.
What have you learnt?

## Slide 81
Voltage/current graphs
A. A filament lamp.
B. A diode.
C. Wires of different materials.
D. A metal resistor.
I
V
I
V
I
V
I
V
1
2
3
4
2
3
1
4

## Slide 82: What are the units of resistance?
Amps
Ohms
Volts
Watts


## Slide 83: What does the circuit symbol shown represent?
Voltmeter
Variable resistor
Light dependent resistor
Thermistor


## Slide 84: If two resistors of 4  and 4  are placed in parallel, what is their total resistance in the circuit?
10 
2 
2.4 
24 


## Slide 85: If a resistor has a potential difference of 10V across it and a current of 0.2 A flowing through it. What is its resistance?
50 
2 
0.5 
15 


## Slide 86
What type of circuit is this?
V
V
series
Name the components
A
Notes: 86
86

## Slide 87
The supply voltage is 6V. What is voltage V1? V2?
V1
V2
10Ω
10Ω
Notes: 87
87

## Slide 88: LAST LESSON
Go through worksheet answers.

## Slide 89: Electrical Charge
Electric charge is given the symbol
Q
Electrons are the charge carriers
that flow in an electrical circuit –
from the negative to positive terminals.
2.21 mins https://www.youtube.com/watch?v=oB1v-wh7EGU

## Slide 90: Electrical Charge EXTENSION
Electrons are so very, very tiny that we measure large groups of them called coulombs. There are 6.25 x 1018 electrons in one coulomb.
The charge on one electron is 1.6 x 10-19 coulombs (C)

## Slide 91: Electrical Charge
The charge on a electron is
1.6 x 10-19C

## Slide 92: REVIEW

## Slide 93: ammeter

## Slide 94: bulb or lamp

## Slide 95: switch

## Slide 96: cell

## Slide 97: voltmeter

## Slide 98: Resistors
The ciruit symbol for a resistor is
Notes: 98
98

## Slide 99: Varying Resistance
A variable resistor can be used to vary the current in a circuit
Notes: 99
99

## Slide 100: Calculate the power
1. A series circuit had a current of 2.0 amps and the voltage of the bulb is 3.0 volts. Calculate the power.
2. A series circuit had a current of 4.5 amps and the voltage of the buzzer is 2.0 volts. Calculate the power.

## Slide 101: Summary
 | CURRENT | VOLTAGE
Measured in |  | 
Measure with |  | 
Amps, A
Voltmeter
Ammeter
Volts, V

## Slide 102: Summary
 | Series | Parallel
Current | SAME | SPLIT
Voltage | SPLIT | SAME

## Slide 103
Match each series circuit to the correct circuit diagram.
A
B
C
1
2
3
3
2
1

## Slide 104
Match
When a lamp is switched on it changes electrical energy into two other kinds of energy. Choose some of these words to fill in the gaps.
The cell has a store of
energy.
The wires transfer
energy from the __
to the .
The lamp transfers the energy as
and energy.
This is the energy source for the circuit.
You need to close this to complete the circuit!
This must be complete (no gaps) for electricity to flow round it.
switch
circuit
cell
electrical
cell
movement
sound
heat
light
lamp
chemical
chemical
electrical
cell
lamp
light
heat

## Slide 105
Both these circuits have the same number of batteries.
Why do the ammeters show different current readings?
Which component has the greater resistance?
There is less current in circuit E which means it's harder for the current to flow in the circuit with the motor.
D
E

## Slide 106
7J Connecting circuits – Circuits quiz
2. The three things needed to make a circuit are a power supply, an electrical device and…
a) wires.
b) a plug.
c) batteries.
1. The parts that are connected to make an electrical circuit are called…
a) computers.
b) components.
c) consonants.
Notes: TEACHER’S NOTES
Answers
1b)
2a)

## Slide 107
3. The flow of electrical charge around a circuit is called the…
a) raisin.
b) battery.
c) current.
7J Connecting circuits – Circuits quiz
4. The symbol represents which electrical component?
a) A switch.
b) A bulb.
c) An ammeter.
Notes: TEACHER’S NOTES
Answers
3c)
4b)

## Slide 108
6. When a switch is closed, an electrical circuit is said to be…
a) complete.
b) broken.
c) positive.
7J Connecting circuits – Circuits quiz
5. What is the symbol for a cell?
a)
b)
c)
Notes: TEACHER’S NOTES
Answers
5b)
6a)

## Slide 109
8. When a circuit is broken, what happens to the current?
a) the current continues to flow.
b) the current changes direction.
c) the current no longer flows.
7. Batteries should be connected so that their poles are arranged…
a) positive to positive.
b) negative to negative.
c) positive to negative.
7J Connecting circuits – Circuits quiz
Notes: TEACHER’S NOTES
Answers
7c)
8c)

## Slide 110: Disadvantages of Series Circuits
When one component breaks the whole circuit stops working as no current flows.
The voltage is divided between the bulbs. so the more bulbs added the dimmer each one is.
The components can’t be switched on and off separately

## Slide 111: Advantages of a Parallel Circuit
When one bulb breaks the rest of the circuit
continues to work.
The voltage in each branch is the same as
the supply voltage. Therefore, bulbs in parallel
will each be as bright as a single bulb.
Each component can be switched on and off separately.

## Slide 112: Resistors in series
4
2
Total resistance = R1 + R2
What is the total resistance for the circuit shown?
Total resistance = R1 + R2
Total resistance = 4  + 2 
Total resistance = 6 

## Slide 113
6
34
What is the total resistance for the circuit shown?
Total resistance = R1 + R2
Total resistance = 6  + 34 
Total resistance = 40 
Resistors in series

## Slide 114: Resistors in parallel
2
4
Total resistance = R1xR2 R1+ R2
Total resistance = 4 x 2
4 + 2
= 1.33
If we connect resistors in parallel the total resistance of the circuit dcreases because there are more branches through which the current can flow.
The total resistance is always smaller than the smallest resistor.

## Slide 115: Resistors in parallel
6
8
What is the total resistance for the circuit shown?
Total resistance = 8 x 6
8 + 6
= 3.4

## Slide 116: Using conductive putty

## Slide 117: Using copper tape

## Slide 118: Using conductive paint